|  | ......................... pcs. .............................. € .............................. € GEZE retractable arm drive K 600 For ventilation or the creation of a stream opening on rectangular, vertically installed inward- and outward-opening bottom-hung, top-hung and side-hung windows as well as skylights and doors. On doors, assembly on the hinge side and opposite hinge side must be guaranteed with unimpeded passage. Assembly either with freely supported lever or fixed connection to the door, the window casement, the lintel, the frame or the door leaf. For convenient use, the combination with GEZE door closers, GEZE motor lock MLS, GEZE emergency exit opener and GEZE RWS as well as the use on escape doors must be guaranteed. High resistance against excess pressure in the direction of closing F>1000N must be observed in order to increase service life. It must be possible to adjust the opening angle individually. The drive must have a soft start and soft stop feature as well as an integrated door locking contact (max. 42 V, 0.5 A). It must be guaranteed that it can be used for the actuation of double-leaf doors with integrated sequence control through activation delay. Technical data: Nominal voltage: 24 V DC Closed circuit current intake: approx. 40 mA Cut-off current : 1.4 A Duty rating: 30% ED Opening angle on the drive: 93° Opening force: 600 N Movement time: approx. 40 s Supply cable: 5 m long; 5x0.5 mm², FRNC-LSIHSI FE 90 Enclosure rating: IP 32 RWA K 600 T freely supported lever with roller ( ) Installation hinge side ( ) Installation opposite hinge side RWA K 600 G lever with guide rail, firmly connected to the door leaf or the window casement ( ) Installation hinge side ( ) Installation opposite hinge side RWA K 600 F lever with link lever, firmly connected to the door leaf or the window casement Installation hinge side Casement dimensions: ........ mm width ........ mm height Leaf weight: ........ kg Colour: ( ) EV1 ( ) Colour according to choice |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € Note: You also need an emergency power control unit GEZE E 260 N or MBZ 300 and accessories. |
|  | ......................... pcs. .............................. € .............................. € Installation and functional test Installation and functional test by an expert authorised by the manufacturer. |
|  | ......................... pcs. .............................. € .............................. € Start-up and official approval Official approval of the complete smoke and heat extraction system by an officially recognised expert, who also hands over the acceptance certificates. |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - compact package Maintenance and testing of hold-open systems (optional position) Service package for maintenance and testing according to ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - Fault diagnosis and repair jobs during the contract period will be carried out at reduced hourly rates - Service technicians will be deployed within 24 hours of the message being received from Monday – Friday between 7 am and 5 pm without surcharges - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 2 years |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - comfort package Service maintenance (optional position) Comfort service package for maintenance and accident prevention inspection in accordance with ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - Extension of the warranty to 36 months (condition: the maintenance contract is concluded 3 months after the commissioning date at the latest) - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - No separate charging for services and travel costs during the warranty period - No separate charging for consumables up to € 25 per maintenance - No separate charging for working hours when spare parts are replaced during the maintenance - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 3 years |
|  | ......................... pcs. .............................. € .............................. € Delivery and installation Wiring to be carried out on site by an electrical contractor according to the GEZE cable plan. Delivery, installation and commissioning through plant fitters or service partner. Safety analysis, instruction of the operator as to how the system works and handing over of the documentation. Annual maintenance and technical inspection by an expert authorised by the manufacturer incl. documentation of the inspection in an inspection log. |