|  | ......................... pcs. .............................. € .............................. € GEZE TSA 325 NT GG all-glass revolving door system in 3- or 4-leaf version, in outstanding transparent design, with freely selectable inside diameter up to 3000 mm, TÜV type-tested in accordance with DIN 18650 with different drive types and many possible configuration options Drive types ( ) Manual operation of the door. or ( ) Manually operated the door with GEZE speed limiter, i.e. the max. speed of rotation of the revolving door is limited by a safety mechanism in the door. or ( ) Manually operated door with GEZE automatic positioning device, i.e. the manual door is moved by a motor at very low speed after passage to the initial position/end position. Safety concept: 1 x Emergency push button in accordance with DIN EN ISO 13850 or ( ) Semi-automatic GEZE Servo drive: Increased passage comfort compared with a manual door thanks to automatic starting of the turnstile. In order to reach walking speed, the turnstile can be overridden by hand. After the door has been passed, it revolves slowly to the final position. Complete drive with control on the interior, control in performance level "c" in accordance with DIN EN ISO 13849-1, convenient parameter setting, commissioning and after-sales service maintenance via optional Bluetooth connection to a PC, power supply: 230 V / 50 Hz / 350 W / 10 A Recommendation: Only if there is a constant range of users Safety concept: 1 x Emergency-stop push button in accordance with DIN EN ISO 13850 or ( ) Fully automatic GEZE revolving door system (triggered via movement detector) Micro-processor controlled, electromechanical drive with infinitely adjustable speed, drive with two pre-set speeds. Complete drive with control on the interior, control in performance level "c" in accordance with DIN EN ISO 13849-1, convenient parameter setting, commissioning and after-sales service maintenance via optional Bluetooth connection to a PC, power supply: 230 V / 50 Hz / 350 W / 10 A, key programme switch for setting the operating modes. Fuse protection in accordance with DIN 18650 (TÜV type-tested and certified) comprising: - Post safety - Emergency stop push button in accordance with DIN EN ISO 13850 - Front post safety (non-contact) - Safety contact strip on the leaf, horizontal (heel protection) - Safety contact strip on the leaf, vertical (hand protection) - Coupled motion safety at the leaf (non-contact, from diameters > 3000 mm) Construction dimensions: ( ) Inside diameter:................. mm (from 1800 mm to 3000) other dimensions on request. ( ) Outside diameter: ......... ..... mm (from 1890 to 3090 mm) ( ) Clear passage height DH: ......mm (up to 3000 mm); other heights on request. ( ) Total height of door system: .............mm ( ) Canopy height: 17.52 mm (height of the glass roof); ( ) Floor recess (min.): 60 mm only for manual door or ( ) Floor recess (min.): 300 mm for door with speed limiter, automatic positioning device, servo and fully automatic. Note: Other dimensions on request. Door position: ( ) central ( ) off-centre, offset in relation to the façade ….. Model type: ( ) triple-leaf ( ) quadruple leaf Turnstile: ( ) rigid door leaf, fine-framed on 3 sides for mounting ESG glass. Drum walls: ( ) Drum walls of curved 16 mm VSG, clear, with vertical edge protection profiles Ceiling construction: ( ) Glass ceiling made of flat 17.52 mm VSG (2 x TVG) clear glass. Outside edges with edge protection. The 2 glass half shells are held by point fittings and have a recess for mounting the swivelling axle bearing. Surface of the light alloy parts: ( ) Powder coating according to RAL or ( ) LM anodised E6/EV1 or ( ) Colour anodised ............ or ( ) Coated with ground stainless steel, grain 240 or ( ) Coated with polished stainless steel Floor ring GEZE 360° stainless steel (V2A) floor ring made of rectangular tubing 30x30x2 mm. The floor ring is used as the floor covering edging at the same time. Dimensions of the drive box: 1404x754x272 mm. ( ) Sheet metal base and/or ( ) Swivel flange (30 x 5 mm) Note: The insulation of the building is a contracted service and must be carried out on site. Floor cover ( ) GEZE clean scraping mat, anthracite colour, 22 mm, more colours available on request! or ( ) Floor cover to be carried out on site Delivery and installation Wiring to be carried out on site according to the GEZE cable plan by an electrical contractor. Installation, commissioning and instruction of the operator as well as documentation handover in compliance with DIN 18650 / EN 16005 through plant fitters or service partner. In compliance with DIN 18650 / EN 16005: - Safety analysis must be carried out as a basis for planning and execution - An inspection must be carried out at least 1 x year and after-sales service maintenance at least 1 x year |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € Night-time closer (optional position) ( ) GEZE night-time closer sliding doors running on the outside, manual, as underfloor guide rollers, box size of underfloor guide rollers in the floor approx. 160 x 175 mm (120° for 3-leaf; 180° for 4-leaf), with connection for on-site drainage, night-time sliding doors made of curved 12 mm VSG, clear, floor latch lock on the sliding panel (on-site profile cylinder), closer from the inside and outside. |
|  | ......................... pcs. .............................. € .............................. € Locking (optional position) ( ) Locking of the turnstile using GEZE extended bolt lock in the door leaf, inclusive profile half cylinder with deadbolt contact Note: When using sliding doors with night-time closers, the turnstile does not need to be locked. |
|  | ......................... pcs. .............................. € .............................. € Handles (optional position) ( ) ground, vertical stainless steel push bars, dia. 30/40 mm, installation directly on the glass or ( ) ground, horizontal stainless steel push bars, dia. 30/40 mm, installation directly on the glass |
|  | ......................... pcs. .............................. € .............................. € Operation (optional position) GEZE key switch to “lock” the programme switch to prevent unauthorised changing of the operating mode, IP rating IP 40 ( ) Surface-mounted ( ) Flush-mounted |
|  | ......................... pcs. .............................. € .............................. € Disabled person's button (optional position) ( ) Delivery and mounting of two GEZE push buttons with wheelchair symbol in the immediate entry area of the revolving door. When this push button is actuated, the revolving speed is reduced to an adjustable value to allow disabled persons a higher degree of access convenience and more safety. The activation duration can also be adjusted. Empty pipes must be routed to the installation point on site. Note: Can only be used with fully automatic version. |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - compact package Maintenance and testing (option) Service package for maintenance and inspection in accordance with EN 16005, DIN 18650 Part 2 and ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - Fault diagnosis and repair jobs during the contract period will be carried out at reduced hourly rates - Service technicians will be deployed within 24 hours of the message being received from Monday – Friday between 7 am and 5 pm without surcharges - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 2 years e.g. GEZE compact service package |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - comfort package Service maintenance (optional position) Comfort service package for maintenance in accordance with EN 16005, DIN 18650 Part 2 and ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - Extension of the warranty to 36 months (condition: the maintenance contract is concluded 3 months after the commissioning date at the latest) - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - No separate charging for services and travel costs during the warranty period - No separate charging for consumables up to EUR 25 per maintenance - No separate charging for working hours when spare parts are replaced during the maintenance - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 3 years |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - exclusive package Service maintenance (optional position) Exclusive service package for servicing, maintenance in accordance with DIN 18650 Part 2 and ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - Extension of the warranty to 60 months (condition: the maintenance contract is concluded 3 months after the commissioning date at the latest) - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - Complete repair: no separate charging for repairs (parts and working hours) and travel costs during the contract run time - Online access for the client to the project and system data at the contractor’s - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 5 years |