|  | ......................... pcs. .............................. € .............................. € GEZE sliding door fitting Perlan 140 Duosync Accessories set for leaf weights up to 140 kg: - synchronous operation of two leaves using only one hand - synchronisation through maintenance-free toothed belt and return pulleys. - Corrosion-proof components Standard version/ scope of supply: Track for direct ceiling installation or wall installation with brackets 4 roller carriages with suspension bolts, 4 carrier plates, 2 floor guide, 4 end stops with 2 hold-open springs 1 toothed belt 2 belt locks 2 driver brackets 2 return pulleys Construction dimensions: Leaf width: ............ mm Area of application: For double-leaf sliding elements |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € Additional buffer (floor or wall attachment) In addition to the end stop, the door leaf must be stopped by a further buffer that is attached either at the middle of the door or at the bottom, so that the door leaf is stopped at the top and bottom at the same time. |
|  | ......................... pcs. .............................. € .............................. € Floor guide with continuous rail |
|  | ......................... pcs. .............................. € .............................. € Clip cover panel made of aluminium As a facing for the track and door suspension plate. To be attached directly on the track using panel fixing brackets (incl.). Colour: ( ) Anodised aluminium ( ) acc. to RAL ( ) for Perlan 140 with wall mounting ( ) for Perlan 140 with ceiling mounting ( ) side parts for wall or ceiling mounting |
|  | ......................... pcs. .............................. € .............................. € Accessories for all-glass sliding doors / glass clamping plates ( ) Clamping plate 200 mm wide made of light metal for glass thickness 8 - 12mm (2 pcs. per leaf) ( ) Continuous glass clamping profile ( ) Floor guide for glass leaf (adjustable) |
|  | ......................... pcs. .............................. € .............................. € Adjustable hold-open mechanism In addition, an adjustable hold-open mechanism can be installed, which can be used to vary the engaging and releasing force. |
|  | ......................... pcs. .............................. € .............................. € GEZE modular fixed panel profile The GEZE fixed panel profile is suitable for bordering fanlights and side parts made of toughened safety glass and can be used as dry glazing for both internal and external applications. The system has been designed for glass thicknesses of 8, 10 and 12 mm. The glass thicknesses are fixed with the identical clamping unit, there is no need for the system to be changed. The threaded nuts for the clamping units contained in the system can be positioned freely in the basic profile and set to the glass edge in accordance with the TRPV (Technical rules for the Design and Construction of Point-Supported Glazing by the German Centre of Competence for Construction). Additional drill holes related to the glass edges or clamping units are not required. The glass panes are set using system-compliant adjusting units which are integrated in the clamping unit and make a tolerance compensation of +/- 2.5 mm possible. Construction components from other manufacturers are not approved for adjustment. In addition, the clamping units can be extended using a safety set for freely suspended glazing. The basic system can be combined with different design clip-on covers. Basic system / Basic profile ( ) Basic profile, aluminium, L = 6,000 mm ( ) Clamping system units, set 20 (20 pieces) adequate for a basic profile L = 6,000 mm, can be used for glass thicknesses of 10 and 12 mm Cover panels, design 40 aluminium (suitable for Patch Fittings, Perlan 140, Levolan etc.) ( ) Clip-on cover profile design 40 set for glass thicknesses of 8 to 12 mm (set = 2 profiles) ( ) Silver-coloured anodised surface ( ) Stainless steel colour anodised surface ( ) End cover cap for profile design 40 ( ) Silver-coloured anodised for glass thicknesses of 8 and 10 mm ( ) Silver-coloured anodised for glass thicknesses of 12 mm ( ) Stainless steel matt for glass thicknesses of 8 and 10 mm ( ) Stainless steel matt for glass thicknesses of 12 mm Cover design Pendulo ( ) Clip-on cover profile design Pendulo for glass thicknesses 8 and 10 mm (2 profiles necessary for 1 base profile) ( ) Silver-coloured anodised surface ( ) Stainless steel colour anodised surface ( ) End cover cap for profile design Pendulo ( ) Silver coloured painted for glass thickness 8 mm ( ) Silver coloured painted for glass thickness 10 mm ( ) Stainless steel optic painted for glass thickness 8 mm ( ) Stainless steel optic painted for glass thickness 10 mm Optional accessories for the modular fixed panel profile ( ) Additional clamping shims (set 40) for glass thicknesses of 8 mm ( ) Clamping system units, set 01 (1 piece) for additional clamping point ( ) Safety version set for fanlights and freely suspending glass panes, adequate for 5 clamping units |